## Slide 1: VEHICLE ISOLATION AND MAINTENANCE

## Slide 2: Truck Key Control
Truck Key Control
Master Spare Key
Storage
Vehicle Repairs
Operational Key Storage
Operational Keys
In use
Operational keys are in 3 states of control – Storage/Driver/Repairer
Notes: Its vital that vehicle safety keys are kept under control and secure to prevent accidental starting and movement of the vehicle whilst someone is working on it

## Slide 3: Master Spare Keys
Stored in secure
locked facility
Stored separately
from running keys
Restricted Access Supervisor, Approved
Staff only
Secured – Locked Storage – Strictly Controlled access
Notes: Master keys should be stored securely to prevent use by unauthorised persons

## Slide 4: Operational keys - Storage
Kept in secure, locked storage facility when not in use or in larger operations a secure control room
Controlled access for drivers and authorised staff only
2 x keys or 1 x Key + Locking fob
Controlled access and security
Notes: When keys are stored its vital that they are secure to prevent them being taken and used by unauthorised persons

## Slide 5: Operational keys - In use
Truck doors locked when cab unattended
If keys needed in ignition – doors locked with 2d Key/Fob
Drivers keep keys secure in use
In ignition or stored in pocket
2 x Operational Keys - Cab access and Keys are kept secure
Vehicle safely parked Handbrake applied
Notes: To prevent unauthorised persons from entering the vehicle – it important that he keys and cab are kept secure

## Slide 6: Vehicle repairs – Onsite
Vehicle:
Safely parked Hand brake on Doors locked Wheels Chocked Vehicle VOR sign
Permit to work SSOW Risk Assessments
Both Running keys handed to repair agent
Keys handed back over by repair agent on job completion
Adequate supervision of repair agent / contractor
Notes: Vehicle maintenance represents potential risks which must be controlled

## Slide 7: Vehicle repair agent safety process
Authorised
Trained Competent
Repair Agent
Site Induction
and sign in
PPE Checked
Safe Systems of Work
Method statements Risk assessments
Work Permit Issued
Vehicle Parked in a safe designated suitable place for the repair
Doors Locked
Handbrakes applied
Vehicle isolated for task
Wheel Chocks Maintenance sign
Cones if required
Plans for Repair Agent to be adequately supervised and kept safe
Operational Keys handed over to repair agent
Adequate supervision of repair agent
Vehicle Repair Completed
Vehicle and Keys handed back
Repair agent signed off Work permit, Site sign in and Job Sheets completed
Notes: A safe system and process is vital to ensure maintenance activities are carried out safely

## Slide 8: Vehicle Maintenance
Maintenance Sign
Vehicle Parked in a safe designated suitable place for the repair
Keys handed to Repair Agent
Doors Locked
Vehicle
Kept
Secure
Controlled
Access
Adequate Supervision
Wheel Chocks
Notes: Adequate and effective controls are key to safe vehicle maintenance