## Slide 1: QNJAC Joint Drill, Blast and Geotechnical Group Tool box talk Overburden Stripping
This toolbox talk is aimed at Quarry Operators, Quarry Managers and Supervisors and should be read in conjunction with the QNJAC Guidance to Managing Change to Excavations and Tips

## Slide 2: Are you Quarrying?
The Quarries Regulations 1999 Regulation 3 (1)
“quarry” means
“subject to paragraph (2) an excavation or system of excavations made for the purpose of, or in connection with, the extraction of minerals or products of minerals.”
Guidance - Drilling and blasting activities relating to overburden stripping for the preparation of an area to be extracted (quarried) is subject to the Quarry Regulations 1999.

## Slide 3: Practical Considerations
Services below on and above ground.
Water, Power, Telecoms, Drains, Sewers.
Surface water features, ditches, drains, underground water courses.
Weak/broken ground due to weathering of top rock.
Uneven floors due to prior extraction and or ripping and removal of loose material.
No established levels to work from, increased input from surveyors to monitor conformance to the design.
Additional road maintenance for blasting vehicles may be required.
Potential increase in buffer/sinking blasting until levels are established.

## Slide 4: Practical Considerations
Often at highest point and on the limit of the site boundary - increased risk of rock being projected outside of quarry demarcated area. Danger zone may well extend outside of the quarry boundary requiring more sentries and temporary closure of public highways/footpaths.
As above, blasting at the site boundary is more likely to give rise to vibration issues at the nearest properties. Additional monitoring or changes to the normal blast design may need to take place.

## Slide 5: Planning Considerations
Volume of overburden strip must be determined .
Desired extraction rate taking into account geotechnical constraints and contingency for weather/site conditions gives an indication of required start date.
Any preparation required prior to bulk blasting e.g. pre-splitting, test holes for electronic initiation.

## Slide 6: Planning Considerations
Adjacent historic faces and/or tips giving rise to stability issues.
Drainage/dewatering plan for new site. Can pipework be installed as faces progress? Do areas earmarked for pipework require smooth/pre split blasting?

## Slide 7: Communication/ Input to process Suggestions for key persons involved:-
Quarry Operator - May need to appoint a blasting contractor (Q Regs 1999 ACOP 189) or additional explosive supervisors (ACOP 188).
Estates Manager - Vibration limits, permitted hours for blasting, out of hours / Bank Holiday exceptions and procedures. Liaising with local councils.
Quarry Manager 8 1(c) appointee - Day to day management of activities. Application of shotfiring rules. Do they need amending to cover overburden blasting? Appointment and authorisation of personnel. Responsible for co-ordinating a team to complete the quarry design (to include overburden stripping).

## Slide 8: Communication/Input to process
Explosives Supervisor - Ensure compliance with blasting parameters set by the Quarry Design team.
Shotfirer - Local knowledge, competency of ground.
Geotechnical Engineer - Face heights, bench widths, face angles, pre split requirements, face orientation, known discontinuities and failure modes, site investigation/borehole data interpretation, volume of materials to be extracted.
Earthworks Contractor - Type and reach of machinery to be employed.