## Slide 1: Positioning a shotfiring shelter Guidance on what to consider when positioning a shotfiring shelter.
Drilling and Blasting
Toolbox Talk : 01
Target Audience
  Shotfirers and Explosives Supervisors.
This toolbox talk may be freely reproduced except for advertising, endorsement or commercial purposes. It has been developed by the Quarries National Joint Advisory Committee (QNJAC) to help quarry operators, contractors, managers and others make health and safety improvements in the quarry industry.
This guidance represents good practice which may go further than the minimum you need to do to comply with the law.
If you use the information provided in this document please acknowledge ‘QNJAC’ as the source .
Updated Feb 2020

## Slide 2: Positioning a shotfiring shelter 1. Introduction
It is best practice to fire a blast from outside of the declared danger zone.
  In this case you do not need a shotfiring shelter
  You will need a remote firing system
If you a firing a blast and need to be inside the declared danger zone then you must use a shotfiring shelter
What is the purpose of a shotfiring shelter ?
  To minimise risk for the shotfirer whilst firing the blast

## Slide 3: Positioning a shotfiring shelter. 2. Construction
How should a shelter be constructed ?
  There are no set guidelines for the construction of a shotfiring shelter, however, there are some obvious factors to be taken into account.
    Should be robust and fitted with a floor
    Should be capable of being moved in a safe manner by on-site equipment
    Should be big enough to hold all the people required
      Good idea to mark with a maximum number
    Should be fitted with an outward opening, closable door
    Should be fitted with an observation slit
    Should be regularly inspected and maintained
    The following slide shows a good example of shelter construction

## Slide 4: Positioning a shotfiring shelter. 2. Construction (continued)
Example of a well constructed shotfiring shelter
Photo courtesy of Aggregate Industries
Robust steel body
Observation slot covered with steel mesh
Strong mesh floor,
helps keep the shelter dry and clean
Strong, outwardly opening door
Carrying system specifically design for on-site equipment
Size : can house 3 people in comfort

## Slide 5: Positioning a shotfiring shelter. 3. Risks
What are the risks ?
  Flyrock
    Impact on shelter
    Ingress through door
  Falls of ground
    From above : impact on shelter or through door
    From below : shelter falls to bench below
  Dust and fumes
    Lung damage
    All persons in a Shotfiring shelter should be provided with suitable dust masks

## Slide 6: Positioning a shotfiring shelter. 4. Basic Guidance (continued)
Distance from blast
  As far as possible
    Limited by the length of the shotfiring cable or shock-tube starter line
  A minimum distance should be specified in the shotfiring rules
DISTANCE – The further the better

## Slide 7: Positioning a shotfiring shelter. 4. Basic Guidance (continued)
Can you fire from outside of the danger zone ?
  This is the best option
  If you can, then you do not need a shelter
  You will need a remote firing system
  This option also gives you greatly enhanced control over the danger zone as you can often fire from a viewing / observation point

## Slide 8: Positioning a shotfiring shelter. 4. Basic Guidance (continued)
Locate shelter behind or to side of blast if possible
  Location should be shown on a plan in the blast specification
BLAST AREA

## Slide 9: Positioning a shotfiring shelter. 4. Basic Guidance (continued)
Distance from crest of bench
  As a guideline this distance should be at least 50% of the face height
  This could be increased if a geotechnical assessment indicates that this is required
h
h/2

## Slide 10: Positioning a shotfiring shelter. 4. Basic Guidance (continued)
Distance from toe of face
  As a guideline this distance should be at least the face height
  This could be increased if a geotechnical assessment indicates that this is required
  If there are multiple benches above then the distance may need to be increased even more
h
h

## Slide 11: Positioning a shotfiring shelter. 4. Basic Guidance (continued)
Orientation of door of shelter
  Facing away from blast
  Parallel to crest of bench
  Parallel to toe of face above
BLAST AREA

## Slide 12: Positioning a shotfiring shelter. 4. Basic Guidance (continued)
Wind direction
  To avoid exposure to dust and fumes the shotfiring shelter should not be downwind of blast
BLAST AREA
WIND DIRECTION

## Slide 13: Positioning a shotfiring shelter. 5. Key Points
Always use a shotfiring shelter
Locate shelter as far away from the blast as possible and to the side or behind the blast
Do not place the shelter down wind of the blast
Locate the shelter away from the crest or toe of any face
Orientate the door of the shelter away from the blast and parallel to the crest and toe of nearby faces