## Slide 1: Danger Zone Control and the Duties of Sentries. Guidance on how to ensure control of the danger zone and what is expected from sentries.
Drilling and Blasting
Toolbox Talk : 07
Updated Feb 2020
Target Audience
  Managers, Supervisors, Shotfirers , Sentries and Explosives Supervisors.
This toolbox talk may be freely reproduced except for advertising, endorsement or commercial purposes. It has been developed by the Quarries National Joint Advisory Committee (QNJAC) to help quarry operators, contractors, managers and others make health and safety improvements in the quarry industry.
This guidance represents good practice which may go further than the minimum you need to do to comply with the law.
If you use the information provided in this document please acknowledge ‘QNJAC’ as the source .

## Slide 2: Danger Zone Control and the Duties of Sentries 1. Introduction
All blasting operations must have a determined danger zone.
For information on Guidance about determining the Danger Zone for Blasting see
  TBT 06 : Defining the Danger Zone for Blasting.
During the firing of a blast the danger zone must be under control and this is enabled by a combination of the use of sentries supplemented by other warning systems such as signs and notices as appropriate.

## Slide 3: Danger Zone Control and the Duties of Sentries 2. Sentries Role
The primary responsibility of a sentry is to
KEEP PEOPLE OUT OF THE DANGER ZONE AND MUST NOT LEAVE THEIR POST UNTIL THE ALL-CLEAR SIGNAL HAS BEEN GIVEN, OR UNTIL THEY ARE RELEASED BY THE PERSON WHO POSTED THEM.

## Slide 4: Danger Zone Control and the Duties of Sentries 3. Sentries
Sentries must be competent to perform their duties and a record kept of training given.
A procedure should be in place to ensure that clear and exact instructions are given to each sentry to ensure they position themselves at the correct location as required in the blast specification
Sentries must be provided with a means of communication with the shotfirer.
It would be wise for sentries to be authorised in writing.

## Slide 5: Danger Zone Control and the Duties of Sentries 4. Communication.
A reliable system of two-way communication must be used to enable the shotfirer and any sentries to maintain contact with each other
The shotfiring rules should include details of the communication process to be followed
  The communication process should include
    Initial contact between the shotfirer and each sentry
    Final two-way check with each sentry
    Firing time radio silence is appropriate except for blasting communications and general site emergency situations
    A separate radio channel for blasting may be appropriate

## Slide 6: Danger Zone Control and the Duties of Sentries 5. Controlling public rights of way.
Many quarries will include public rights of way inside of the danger zone for blasting
  Roads, Footpaths, Bridle Ways, Canals etc.
Each right of way will require a sentry at each location where the right of way enters / exits the danger zone
  There needs to be a process to ensure that there is nobody on the right of way before it is closed. This is best achieved by a walk or drive through
It is not permissible for sentries to close any public right of way but users can be advised that blasting is about to take place and asked not to pass the sentry position
  If any person insists on entering the danger zone then the sentry must immediately inform the shotfirer
The above principle also applies to premises not under the control for the quarry.

## Slide 7: Danger Zone Control and the Duties of Sentries 6. Key Points.
Understand your duties
Stay out of the danger zone.
Keep unauthorised people out of the danger zone.
Maintain communication.
If you cannot do all of these, stop the blast.