## Slide 1: The Post-Blast Inspection Guidance on the post-blast inspection process
Drilling and Blasting
Toolbox Talk : 08
Target Audience
  Shotfirers and Explosive Supervisors.
This toolbox talk may be freely reproduced except for advertising, endorsement or commercial purposes. It has been developed by the Quarries National Joint Advisory Committee (QNJAC) to help quarry operators, contractors, managers and others make health and safety improvements in the quarry industry.
This guidance represents good practice which may go further than the minimum you need to do to comply with the law.
If you use the information provided in this document please acknowledge ‘QNJAC’ as the source .
Updated Feb 2020

## Slide 2: The Post-Blast Inspection 1. Introduction
The Shotfirer has a responsibility to carry out a post-blast inspection
  The purpose of the inspection is to confirm that conditions are safe for work in the area to recommence
  In particular the shotfirer is looking for evidence of misfires and unsafe ground conditions
  Where a dangerous condition has resulted from the blast the shotfirer should maintain the Danger Zone and inform the Explosives Supervisor as soon as possible
  Shotfirers need to follow the manufacturers recommended minimum time after firing before carrying out the inspection particularly when using electronic detonators
Most safety professionals consider the post-blast inspection to be the most hazardous part of the shotfiring job

## Slide 3: The Post-Blast Inspection 2. What are the hazards
Fumes and dust
  All blasts will produce fumes and this is often accompanied by dust
  Both fumes and dust in excessive quantities can be harmful to health and exposure to them should be avoided
    See QNJAC TBT No 16 Post Blast Fumes
WAIT UNTIL THE DUST AND
FUMES HAVE CLEARED

## Slide 4: The Post-Blast Inspection 2. What are the hazards
Falls of ground
  The blasting process inevitably results in some movement of the rock mass for some considerable distance from the blast area
  This can lead to falls of ground from both the benches above and below the blast
  These falls of ground can happen some considerable time after the blast has been fired and pose a serious threat to the safety of the shotfirer and any other personnel in the area

## Slide 5: The Post-Blast Inspection 2. What are the hazards
Falls of ground
  The area of ground immediately surrounding the blast area can be especially unstable
  On buffer blasts care needs to be taken walking over the heaved up and fractured blasted area
  It is not unusual for overhangs to be left behind on the newly formed crest
  Edge protection should be placed behind and to the side of the shot before it is fired if possible
  The face will not have been ‘dressed’

## Slide 6: The Post-Blast Inspection 2. What are the hazards
Slips, trips and falls
  The shotfirer needs to take great care when walking around and inspecting the blast due to uneven ground, voids and rocks they may encounter
Misfires or burning explosives
  If the shotfirer discovers explosives that have either misfired or are burning then there is a clear danger of additional detonations with the associated risks of blast damage and flyrock
  In such cases the shotfirer should note their positions and
    Return to the shotfiring shelter
    Ensure that the all-clear is not sounded
    Ensure that all sentries stay in-place
    Inform the Explosives Supervisor of the situation
  The Shotfiring Rules for each quarry should include a section dealing with misfires and it is these procedures that should be followed in this event

## Slide 7: The Post-Blast Inspection 3. Minimising the risks
Fumes and dust
  Make sure the shotfiring shelter is not positioned downwind of the blast area
    See QNJAC TBT 01 Positioning a Shotfiring Shelter
  Wait for the fumes and dust to clear
Falls of ground
  Keep away from the toe of the face above and crest of the face below
  If possible inspect the blast muck-pile from the bench below
  Blasting may expose cavities in limestone quarries or old workings in opencast sites
  Inspect the blast muck-pile from the side

## Slide 8: The Post-Blast Inspection 4. Key points
The post-blast inspection is potentially the most risky part of the shotfiring process
After firing wait until the dust and fumes have cleared, following the manufacturers guidance on minimum times before inspecting
Approach the blast area with care avoiding the toes and crest of faces
Inspect the blast area from below or from the side of the blast
Do not rush the inspection process
Carry out the inspection in pairs, if not possible stay in communication
Do not sound the all-clear until the inspection process is complete