## Slide 1: Thunderstorms – Risks and Actions Guidance on what steps to take if a thunderstorm approaches during the blasting process.
Drilling and Blasting
Toolbox Talk : 11
Target Audience
  Anybody involved in the blasting process.
This toolbox talk may be freely reproduced except for advertising, endorsement or commercial purposes. It has been developed by the Quarries National Joint Advisory Committee (QNJAC) to help quarry operators, contractors, managers and others make health and safety improvements in the quarry industry.
This guidance represents good practice which may go further than the minimum you need to do to comply with the law.
If you use the information provided in this document please acknowledge ‘QNJAC’ as the source .
Updated Sep 2019

## Slide 2: Thunderstorms – Risks and Actions 1. Introduction
Thunderstorms are a serious threat to drilling and blasting operations
Each year on average in the UK there are
  300,000 ground strikes by lightning
  50 people struck by lightning
  3 people killed by lightning
A direct ground strike on a blast can result in the blast being partially or completely initiated
Additional information on personal safety in thunder storms can be found at https://www.rospa.com/leisure-safety/advice/lightning/
Notes: https://www.rospa.com/leisure-safety/advice/lightning/
Sep 2019

## Slide 3: Thunderstorms – Risks and Actions 2. The Risks.
There are two issues relating to thunderstorms and the drilling and blasting operations
  Personal Safety
    Risk of being struck by lightning
  Safety of the Blast
    Unintended initiation of the blast or part of the blast

## Slide 4: Thunderstorms – Risks and Actions 2. The Risks cont.
There is no safe distance from a lightning strike because the location of the next strike is unpredictable
Do not make the mistake of thinking you are safe just because you are using a non-electric initiation system as a direct strike could still cause part or all of the blast to initiate

## Slide 5: Thunderstorms – Risks and Actions 4. When to Take Action.
Consider checking the weather forecast before you start to load the blast or use one of the internet based, real-time, lightning warning services
As soon as you hear thunder or see lightning you should take precautionary measures as outlined below.
Do not return to work until all involved agree it is safe to do so and as instructed by the Responsible Person.

## Slide 6: Thunderstorms – Risks and Actions 3. Precautionary Action, General Safety.
Standing outside anywhere in a quarry during a thunderstorm puts you at risk
The Responsible Person should be informed of the situation as soon as practicable.
You should move to a sheltered place
  Rubber tyred vehicle (not carrying explosives or detonators)
  Building
If you are caught in the open
  Crouch down and keep your head as low as possible

## Slide 7: Thunderstorms – Risks and Actions 4. Precautionary Action, Safety of the Blast.
Explosives and accessories outside anywhere in a quarry during a thunderstorm can be initiated by electrical activity from the storm.
The Responsible Person should be informed of the situation as soon as practicable.
The area of the blast should be immediately evacuated
A danger zone should be established as if the blast were to be fired

## Slide 8: Thunderstorms – Risks and Actions 6. Key Points.
Do not work in the open during a thunderstorm
When a thunderstorm approaches you should
  Inform the Responsible Person as soon as practicable.
  Evacuate the blast area, establish and secure the danger zone
  Take shelter inside a building or rubber tyred vehicle
Do not return to work until instructed by the Responsible Person that it is safe to do so.