## Slide 1: Post-Blast Fumes Guidance on post-blast fumes and the steps to be taken to help reduce their production and avoid exposure to them.
Drilling and Blasting
Toolbox Talk : 16
Target Audience
  All those involved in the blasting operation – especially the post-blast inspection process.
This toolbox talk may be freely reproduced except for advertising, endorsement or commercial purposes. It has been developed by the Quarries National Joint Advisory Committee (QNJAC) to help quarry operators, contractors, managers and others make health and safety improvements in the quarry industry.
This guidance represents good practice which may go further than the minimum you need to do to comply with the law.
If you use the information provided in this document please acknowledge ‘QNJAC’ as the source .
Updated July 2019

## Slide 2: Post-Blast Fumes 1. Introduction
All explosives will produce post-blast fumes
  In the order of 850 to 1,000 litres of gas are generated per kilogramme of explosive detonated
  So a blast containing 5 tonnes of explosive can produce up to 5 million litres of gas in about 1 second
For the most part these fumes will consist of a combination of the following gases and vapours which are largely invisible
  Carbon Dioxide
  Nitrogen
  Water Vapour (Steam)
Whilst these gases do not support life they are not toxic.

## Slide 3: Post-Blast Fumes 1. Introduction
The ranges of the major components produced from explosives and their physiological effect are shown in the following table
Owing to their toxicity, particular attention is paid to concentrations of CO and NOx – for surface operations NOx is the more serious danger

## Slide 4: Post-Blast Fumes 2. Toxic Fumes
Under ‘Normal’ conditions a small portion of the post-blast fumes produced are toxic including
  Oxides of Nitrogen : commonly known as NOx and often seen as orange/brown fumes
  Carbon Monoxide, which is a colourless and odourless gas
  Particles of explosive residue
Under ‘Abnormal’ conditions, where complete decomposition of, for example, ammonium nitrate in ANFO, does not take place, perhaps 75 to 125 litres of NOx are produced per kilogramme of explosive, on occasions greater.
NOx are approximately 50% heavier than air and hence in calm or light wind conditions can congregate in low lying areas where they pose a serious risk. CO is slightly lighter than air but short lived and usually quickly disperses

## Slide 5: Post-Blast Fumes 2. Toxic Fumes
Fumes should not be tolerated where they can put workers, the public and wildlife at serious risk of health damage or even death

## Slide 6: Post-Blast Fumes 3. Factors Increasing the Level of Toxic Fumes
Fumes could cause permanent damage to your health
  NOx can turn into acid inside your lungs. This causes blisters than can burst several days later and cause death by ‘drowning’
  Carbon Monoxide replaces oxygen in your blood and is thus poisonous
Manufacturers of explosives will design their products to be close to being ‘Oxygen Balanced’
  That is there is just enough oxygen in the product to turn all the fuel into carbon dioxide
  If this balance is upset then the level of toxic fume will increase
    Reduced fuel or increased oxygen gives increased NOx
    Increased fuel or reduced oxygen gives increased Carbon Monoxide

## Slide 7: Post-Blast Fumes 3. Factors Increasing the Level of Toxic Fumes
If for some reason the explosive does not perform as expected then this can also result in increased post-blast toxic fume production
  Examples of this which can be controlled are:
    Shock/gas desensitisation of the explosive during the blast and general poor attention to blast design principles
    Inadequate confinement at the time the hole is detonated
    Inadequate priming of the explosive
    Poor choice of explosives, use of old or contaminated products or lack of control of on-site product mixing
  Such problems are often indicated by NOx being generated from a specific part of the blast only
  Examples difficult to control and which may occur across the whole shot are reactivity of the explosives with the rock and hot products of reaction meeting a cold atmosphere
  It is difficult to avoid the occasional generation of fumes in this manner and you should always therefore presume that the post-blast fume cloud is likely to contain toxic fumes

## Slide 8: Post-Blast Fumes 3. Factors Increasing the Level of Toxic Fume
Site-mixed ANFO
  ANFO needs 5.6% of fuel oil by weight to be oxygen balanced
  Reduced fuel gives NOx
  Increased fuel gives Carbon Monoxide
  Inadequate mixing of the ANFO will also increase the level of fume
  Wet AN, poor absorbent quality of the AN prills and a high level of ammonium nitrate fines can also add to fume generation
  Shotfiring rules should cover the procedure used when site-mixing ANFO
Water ingress into ANFO and ‘churning’ when bulk emulsion loading
  ANFO is not waterproof: if ANFO comes into contact with water in a wet or damp hole then the level of NOx in post-blast fumes will greatly increase
  Poor bulk emulsion hose handling practices: too fast withdrawal or top loading wet holes can cause mixing/churning of water and mud with explosive

## Slide 9: Post-Blast Fumes 4. Exposure to post-blast fumes
In the event of someone who has been exposed to post-blast fumes feeling unwell immediate medical assistance should be sought
  Respiratory symptoms may take some time to develop
  The medical practitioner should be made aware of the potential exposure to NOx and Carbon Monoxide
  Fatal Incident
  In the Philippines in 2006, a shotfirer was conducting a post-blast inspection at a quarry when he fell into a cavity. He was rescued and taken to hospital with apparently only minor injuries. At the time of his rescue, it was noticed that his breathing was laboured, but this information was not passed on to the hospital staff. He died the next day of severe pulmonary oedema (NOx poisoning), which was not recognised by either the medical team or operational staff.

## Slide 10: Post-Blast Fumes 5. Key Points
Always follow the guidance given by the manufacturer relating to the conditions for use of explosive products and the method of loading and priming
Never use ANFO in a wet or damp hole and always ensure that site-mixed ANFO is correctly and completely mixed with the correct proportion of AN to fuel
Leave sufficient time for fumes to clear before carrying out a post-blast inspection
Be aware of the potential health effects of exposure to post-blast fumes
  Medical practitioners should be made aware of the potential exposure to NOx and Carbon Monoxide

## Slide 11: Post-Blast Fumes 5. Key Points
The underlying causes of high NOx are fuel-deficiency in the explosive or detonation reactions that do not continue to completion. Therefore always:
  Use the correct product for the job
  Pay attention to mixing, loading and priming practices
  Stem and confine the explosives well
  … and remember, poor confinement creates problems other than fumes!